## Slide 1: Embedded Systems Orientation Phase
Introduction

## Slide 2: Learning outcomes
You develop and program interactive embedded systems with sensors and actuators using different I/O programming techniques.

## Slide 3: Teachers
Gerald Hilderink room 2.42 g.hilderink@fontys.nl
Jaap Geurts
Sabina Pencheva
Stan van Hartingsveldt
Qin Zhao
Xuemei Pu

## Slide 4: Course Structure - Orientation Phase
Week 1-6 and 7-12  two half days per week
Lessons
Exercises
Week 6 and 12
Assessment weeks

## Slide 5: Course Structure – Advanced Phase
Week 13-16  two half days per week
Lessons & assignments (60% time)
Project & workshops (40% time)
Week 17-18
Assessment week
Final delivery of projects:
product
documentation
presentation

## Slide 6: Week Overview
Introduction to Arduino Sketch
Introduction to Rich-Shield
Introduction to Programming
Communication
Examples
Notes: Boring because context is not given yet  hidden for now, the Week Overview will come back after the introduction.

## Slide 7
Embedded Systems are Everywhere

## Slide 8: Embedded Systems
What is an Embedded System?
An embedded system is a controller with a dedicated function embedded within a larger mechanical or electrical system to automate real-time processes. This is a device including hardware, software and mechanical parts.
Notes: Can you think of an embedded system (not in the picture) that you are using in your daily life?
Is a laptop or desktop computer an embedded system? Answer: no, it’s not part of a device or apparatus.
Is your smartphone an embedded system? Answer: no, same reason as for laptop, but it can communicate with an embedded system via an app.

## Slide 9: Embedded Systems
What is Embedded System Engineering?
Embedded System Engineering is multidisciplinary field of expertise required to automate processes with embedded systems.
It consists of
Software engineering
Computer engineering
Electrical engineering
Control engineering
Physics
Notes: Use picture to imagine the multiple disciplines on a drone.

## Slide 10: Arduino
We will use the Arduino platform at the heart of the embedded systems we are going to develop in this course.
The Arduino is a cheap and easy-to-learn platform, and conceptually similar to industrial Embedded Systems.
There are several types of Arduinos available from tiny, small, compact to large.
- Uno, Leonardo, Mega, Nano, Mini, Tiny and more

## Slide 11: Arduino
What is Arduino?
“Arduino is an open-source electronics platform based on easy-to-use hardware and software. It's intended for anyone making interactive projects.”

## Slide 13: Arduino – Hardware
General Purpose Input Output (GPIO) headers (R3)
Reset button
USB port
LEDs
External power port
Power electronics
Microcontroller + memory
Serial port electronics
GPIO headers (R3)
Serial port electronics

## Slide 14: Arduino – Microcontroller
Small computer on a single Chip
Energy efficient microprocessor (CPU)
Programmable memory
Serial ports (one USB for programming)
I/O pins to connect sensors and actuators
Special features on Chip (advanced)
Many Arduino boards with different types of microcontrollers available with different speeds, capacities and features.
Notes: No external devices:
No keyboard
No mouse
No screen

## Slide 15: Arduino – Shields
Arduino supports many different types of additional modules called “Shields”.
Motor control (3D printer)
Data monitoring
Internet of Things

## Slide 16: Arduino – Programming
Let’s learn how to program the Arduino in C

## Slide 17: Arduino – Programming
Arduino needs a program to work.
The place to find information and tools is www.arduino.cc
We use the Arduino IDE tool to write, build, upload and debug programs.
 Download and install the Arduino IDE (download) from the www.arduino.cc website on your laptop ...
IDE = Integrated Development Environment

## Slide 18: Arduino IDE
 Plug in your Arduino in the USB port … (you hear a bleep)
 Start the Arduino IDE …

## Slide 19: Arduino IDE – Setup
Connect the Arduino to your laptop using the USB cable.
Set up:
 Tools  Board  Leonardo or Uno
 Tools  Port  Arduino com port
 Tools  Programmer  AVRISP mkII
Important! Select the right board!

## Slide 20: Arduino IDE – Blink demo
Select:
 File  Examples  01.Basics  Blink
The Blink example loads in a new editor.
Build and upload the example:
 Press and observe the LEDs on Arduino
If the LED blinks on the Arduino then it’s OK otherwise troubleshooting…
Notes: Show students how to start Arduino, configure it and run the first blink example demo.
Show them how to copy the rich-shield library and examples

## Slide 21: Arduino IDE – Blink demo
Notes: Show students how to start Arduino, configure it and run the first blink example demo.
Show them how to copy the rich-shield library and examples

## Slide 22: Arduino IDE – New Sketch
 Start a new Sketch …
Syntax highlighting improves readability
keywords
comments
structural characters
Notes: Discuss the code example. Explain the functions setup() and loop(). Explain highlighting, keywords, structural characters (braces), comments, and the place to put in your code.

## Slide 23: Serial communication
Serial communication passes the characters one-by-one with a pattern of serial bits
Information is transmitted as zeros (‘0’) and ones (‘1’) …. also known as bits.
Electrical signal combining clock (baud-rate) and data
USB

## Slide 24: Serial communication
The laptop and Arduino communicate via the USB cable (Universal Serial Bus)
Powers the Arduino (+5V, 0V)
Upload program to the Arduino
Send messages to the Arduino
Receive messages from the Arduino
It’s useful to send feedback of the program state on the Arduino to the serial monitor on the laptop  to solve run-errors (=debugging)

## Slide 25: Serial communication
void setup()
{
// Set serial speed
Serial.begin(9600);
}
void loop()
{
// Send a string to the serial monitor
Serial.print(“Hello World!");
}
Use previous sketch or create new
 Edit the program
 Build and upload the program
 Open the serial monitor (baudrate must be 9600)
 What do you see?
 Replace print into println
 Repeat steps 3..5

## Slide 26: Serial Communication – Getting feedback
void setup()
{
Serial.begin(9600); // Serial speed
// … your code here
Serial.println(“Initialized”); // send state
}
void loop()
{
// … your code here
Serial.println("It's working"); // send state
}

## Slide 27: Programming – Basic steps
Create new sketch
Load example
Load existing sketch
Edit code
Build
Upload hex to Arduino
Syntax errors?
Yes, correct errors
No
Ready editing
Save sketch
Yeah!
No, improve program
Start
End
or
or
Working as intended?
Yes