## Slide 1: Embedded Systems
Analog I/O
Variable scope
Operators

## Slide 2: Week overview
Analog I/O
Potentiometer
Variable scope
Operators

## Slide 3: Recap
Digital I/O
Input is either HIGH/LOW (on/off).
We can ‘sense/measure’ many things digitally
E.g.
Elevator door open/closed
Speed (how?)
Location of a bottle in plant
Reading a bar-code
Computer mouse motion
Notes: Ask students how speed could be “sensed”?

## Slide 4: Analog Input
The world is mostly analog. I.e. not On or Off, but something in between.
E.g.
Temperature, Brightness, Pressure, Audio volume, etc.

## Slide 5
Analog – continuous time and continuous value from very quiet to extremely loud (and everything in between) – infinite number of values
Digital – discrete time and quantized value button pressed or not, or music on CD or USB stick – finite number of values
binary
MP3
WAV
FLAC
AIFF MP4
MKV MPEG
Digital data stream or storage on CD, USB, HDD, Cloud, etc.
Analog signal sampling
Digital data
binary
ADC
Signal is analog
Input is analog
Notes: Definition: An analog signal is a continuous wave denoted by a sine wave and may vary in signal strength (amplitude) or frequency (time). Most analog signals are a composition of different sine waves.

## Slide 6: Digital data and analog signal
Signal is analog
Input is digital (on/off)
Notes: Definition: An analog signal is a continuous wave denoted by a sine wave and may vary in signal strength (amplitude) or frequency (time). Most analog signals are a composition of different sine waves.

## Slide 7: How to measure analog?
Example:
Intake gate for hydroelectric plant.
How far is a gate open?

## Slide 8: Analog Input
Attach many switches to the fence.
Now we have 4 levels

## Slide 9
4 switches = not very efficient.
Suppose we want to know 100 levels

## Slide 10: Analog Input
The inlet fence
Connect a potentiometer to the fence

## Slide 11: Analog I/O
Arduino has a dedicated port for reading an analog I/O
Use a potentiometer

## Slide 12: Reading a potentiometer
Values run from 0 – 1023
Connected to Analog Input
Configure port:
pinMode(POTPIN, INPUT);
read value with:
val = analogRead(POTPIN);

## Slide 13: Example code
const int POTPIN = 0;
int val = 0;
void setup()
{
pinMode(POTPIN, INPUT);
pinMode(LEDPIN, OUTPUT);
}
void loop()
{
val = analogRead(POTPIN);
digitalWrite(LEDPIN, HIGH);
delay(val);
digitalWrite(LEDPIN, LOW);
delay(val);
}

## Slide 14: Variables Revisited

## Slide 15: Variable declaration & initialization
int i;
i = 0;
int i = 0;
int k, l;
int k = 0, l = 0;
Valid characters are: a-z, A-Z, 0-9, _ (=underscore)
Names must start with a letter(small or capital)
Uninitialized variables have an undefined value
Declare variable closest to place of first use

## Slide 16: Variables in C
Basic types
[unsigned] char
[unsigned] short
[unsigned] int
[unsigned] long
[unsigned] long long
float
double
Minimum (actual size depends)
8 bit (0-255, -127-127)
16 bit (0-65535, -32767-32767)
16 bit
32 bit (0-4294967295)
64 bit (0-18446744073709551615)
32 bit
64 bit
Notes: The actual size depends on the processor. int could be 16bit or 32bit

## Slide 17: Better types
int8_t
uint8_t
int16_t
uint16_t
int32_t
uint32_t
8 bit int signed
8 bit int unsigned
etc.

## Slide 18: Constants
variables can be made constant
const int P_LED1 = 12;
old way of doing this:
#define P_LED1 12

## Slide 19: Variables have scope
Block Scope
Local to the block
(can’t be accessed outside)
Global scope
Global to the program
(access anywhere)

## Slide 20: Scope of variables
block scope, only valid between the matching { and }
global scope, valid in the whole program
In C you can only use a variable in the scope in which it is declared.
there are two kinds:

## Slide 21: Scope of variables (II)
void loop()
{
if (LED_OFF)
{
int i = 10;
while (i < 14)
{
digitalWrite(i, LOW);
i++;
}
}
}
void loop()
{
int i = 10;
if (LED_OFF)
{
while (i < 14)
{
digitalWrite(i, LOW);
i++;
}
}
}
good practice: make the scope as small as possible

## Slide 22: Scope of variables (III)
void setup()
{
int nrofLeds = 3;
}
void loop()
{
int i = 0;
while (i < nrofLeds)
{
digitalWrite(LEDPIN0 + i, HIGH);
i++;
}
}
nrofLeds is unknown in this scope!
Notes: Buiten de block scope is de variabele NIET bekend.
Hoe het probleem in dit voorbeeld op te lossen: globale scope

## Slide 23: Global variables
const int nrofLeds = 3;
void loop()
{
int i = 0;
while (i < nrofLeds)
{
digitalWrite(LEDPIN0 + i, HIGH);
i++;
}
}

## Slide 24: Good practice: coding standard (I)
Coding standard = rules to write good software
In an if, always use { and }, even if there is only one statement inside
if (i > 15)
{
digitalWrite(LEDPIN, HIGH);
}

## Slide 25: Good practice: coding standard (II)
{ and } are always on a new line
indent the code in the block
between { and }
use spaces around the operators:
+, -, /, ||, &&, etc.
if ((i > 15) && (k < 100))
{
digitalWrite(LEDPIN, HIGH);
delay(100);
}
tip: Ctrl-T for auto-format in the Arduino IDE

## Slide 26: Operators
c = a + b
a = a - b
c = a++
a = ++a
c = a--
a = --a
a -= b
b += c
=
!=
<
>
<=
>=
&&
||

## Slide 27: Resources
https://en.wikipedia.org/wiki/C_data_types#Basic_types
https://en.cppreference.com/w/c/types/integer