## Slide 1: Embedded Students

## Slide 2: Analog components
LDR
Light Dependent Resistor
like a potmeter but changes according to amount of light.

## Slide 3: Explain LDR
The resistance of an LDR changes depending on how much light falls onto it.
analogRead() will return a different value depending on light intensity.
More light  less resistance  higher value returned.

## Slide 4: LDR usage
const int LDR_IN = 14;
const int LIGHT_THRESHOLD = 82;
int brightness = analogRead(LDR_IN);
if (brightness > LIGHT_THRESHOLD)
// too bright
else
// normal

## Slide 5: Analog Input
NTC
Negative Temperature Coefficient
Like a potmeter but changes according to temperature

## Slide 6: NTC
The resistance of an NTC changes with temperature.
analogRead() will return a different value depending on light intensity.
More heat  lower resistance  higher value read

## Slide 7: NTC usage
const int NTC_IN = 15;
const int TEMP_THRESHOLD = 149;
int temp = analogRead(NTC_IN);
if (temp > TEMP_THRESHOLD)
// too hot
else
// normal

## Slide 8: Reading analog values
What if the read value is close to the threshold?
The real world isn’t discreet nor constant.
The read value will hover around the threshold

## Slide 9: Threshold hovering solved
const int UPPER = 149;
const int LOWER = 125;
bool warning = false;
void loop() {
int temp = analogRead(NTC_IN);
if (!warning && temp > UPPER)
warning = true;
else if (warning && temp < LOWER)
warning = false;
// else don't change anything
}

## Slide 10: Buzzer

## Slide 11: Digital
Buzzer
Piezo electric device
produces sound when a (fixed) waveform is applied.

## Slide 12: Piezo electric effect
A voltage is applied to a two layer membrane which contracts or expands.
Motion  air movement  sound!

## Slide 13: Buzzer
If we quickly expand and contract we produce a sound wave.
Typical frequency: 440Hz (for an A)

## Slide 14: Sound with Arduino
We could do this ourselves.
But is limited in range and precision.
Code is busy while playing (i.e. can’t do anything else while playing a tone)
digitalWrite(BUZZER, HIGH);
// @ 440hz period is 2.2ms
// 2.2 / 2 = 1ms
delay(1);
digitalWrite(BUZZER, LOW);
delay(1);

## Slide 15: Sound with Arduino
The tone() function is specifically used for buzzers.
tone(pin, frequency, duration);
where
pin is the pin the buzzer is connected to
frequency is in Hz
duration is in ms

## Slide 16: Code readability

## Slide 17: Code readability
Better names improve code readability:
int button1_state;
/// ...
if (digitalRead(K1) == LOW)
button1_state = 1;
else
button1_state = 0
Should not use magic numbers:
button1_state = 1;
replace with:
const int PUSHED = 1;
/// ...
button1_state = PUSHED;

## Slide 18: Enum type
We can improve this with an enum type:
enum button_state { PUSHED, RELEASED };
enum button_state button1 = RELEASED;
void loop()
{
}

## Slide 19: Variables & Types
float temp_inside = 22.3;
float temp_outside = 15.8;
/* The range & unit is unknown*/
celsius temp_inside = 22.3;
celsius temp_outside = 15.8;
/* it is clear what the range & unit is */
Creating a new type helps code readability:
Compare:
Notes: Explain left example we don’t know the range. because int = -32767 + 32767

## Slide 20: New types
How to create a new type:
From here on celsius can be used.
typedef float celsius;
void setup()
{
}
void loop()
{
celsius inside_temp = 22.5;
}