## Slide 1: IEO – week 8

## Slide 2: This week
Internet Protocol
Internet Addressing
Subnet
Notes: Applies to al electronic devices?

## Slide 3: Layered Communication: TCP/IP Protocols Overview
Physical Layer
DataLink Layer
Network Layer
Transport Layer
Application Layer
HTTP
DHCP
FTP
DNS
DHCP
Telnet
SMTP
TCP
UDP
IP
Ethernet
Wifi
Bluetooth
Bluetooth
Wifi
Ethernet

## Slide 4: IP Protocol
Layer 3 (Network layer) Protocol
Connectionless Protocol
Unreliable
Best Effort Service
Delivers Datagrams
Responsible for Routing

## Slide 5: IP Addressing
192
68
1
125
192.68.1.125
11000000
01000100
00000001
01111101
32 bits

## Slide 6: IP Addressing
IPv4 :
232 = 4 294 967 296 addresses

## Slide 7: IP Addressing
192
68
1
125
192.68.1.125
Network id
Host id

## Slide 8: IP Classful Addressing
History :
Network ID was 8 bits
How many hosts could we then address ?
224-2
… but only 28 (256) subnets

## Slide 9: IP Classful Addressing
Later :
To accommodate more networks Classful Addressing was used
  More flexibility in the number of networks to be used

## Slide 10: IP Classful Addressing

## Slide 11: IP Addressing
Now :
To allow even more flexibility in IP addressing
  IP Classless Addressing

## Slide 12: IP CIDR (Classless Inter Domain Routing) Addressing
192
68
1
125
192.168.1.125/24
Network id
Host id
11111111.11111111.11111111.00000000
Subnet Mask :

## Slide 13: IP Subnetting
192
68
1
125
192.68.1.125/255.255.255.0
Network id
Host id
11111111.11111111.11111111.00000000
Subnet Mask :
255.255.255.0
or

## Slide 14: IP Subnetting
192
68
1
125
192.68.1.125/24
Network id
Host id
192.168.1.0
Network :
Hosts :
2n-2 = 28-2 = 254

## Slide 15: IP Addressing
Host ID consisting of all 0s or all 1s are special, they can’t be used for assigning a host
Host id consisting of all 0s is used to assign the whole network, in our example it is : 192.168.1.0
Host id consisting of all 1s is used to assign broadcast address, in our example it is : 192.168.1.255

## Slide 16: IP Addressing
Special Address Ranges :
10.0.0.0/8 (private networks)
192.168.0.0/16 (private networks)
172.16.0.0/12 (private networks)
169.254.0.0/16 (link-local addresses)
127.0.0.0/8 (loopback addresses)

## Slide 17: ARP: Address Resolution Protocol
ARP does address resolution between an IP address and hardware MAC address within LAN network

## Slide 18: ARP Protocol

## Slide 19: ARP Protocol

## Slide 20: ICMP Protocol
The Internet Control Message Protocol is used by the network devices to send error messages indicating, for example, non-availability of a requested service.
The ICMP can also be used for the network diagnosis (the ping command).

## Slide 21: ICMP : Ping and Traceroute

## Slide 22: Several useful Linux networking commands
Configure network interfaces:
ifconfig command
Example:
ifconfig eth0 192.168.1.2 netmask 255.255.255.0
Configure eth0 interface with an IP address and subnet mask.
ifconfig -a
Show all network interfaces of this machine.

## Slide 23: Several useful Linux networking commands
Configure network interfaces:
ip command
Example:
ip addr add 192.168.1.2/24 dev eth0
Configure eth0 interface with an IP address and subnet mask.
ip addr show
Show all network interfaces of this machine.

## Slide 24: Several useful Linux networking commands
Manipulate the system arp cache:
arp command
Example:
arp
Show current ARP cache entries.
arp –d 192.168.1.1
Delete ARP cache entry for the IP address 192.168.1.1.

## Slide 25: Several useful Linux networking commands
Network Diagnosis:
ping command
Example:
ping 192.168.1.1
Send ICMP Echo Request (ping) to 192.168.1.1 to see whether the node 192.168.1.1 is alive.

## Slide 26: Several useful Linux networking commands
Print the route a packet follows to the destination
traceroute command
Example:
traceroute 192.168.1.1
Shows the IP addresses of the hops leading to the IP address 192.168.1.1

## Slide 27: Questions?