## Slide 1: IEO – week 3

## Slide 2: This week
How data is stored in computers?
How does a computer handle negative numbers?
Notes: Applies to al electronic devices?

## Slide 3: Memory
Computer Data Storage

## Slide 4: Storage/Memory
Fundamental component of a computer
    Required to store data and run applications
Retain digital data, which are manipulated by CPU
Various types and forms
    Consists of computer components and recording media

## Slide 5: Storage types & medium
Optical
  CD
  DVD
  Blu-Ray …
Magnetic
  Floppy
  Hard Drives …
Flash Memory
  SSD
  Memory sticks/cards …
Notes: Image: http://www.pcworld.com/article/2106260/sony-panasonic-develop-300gb-optical-discs-for-enterprise-storage.html

## Slide 6: Memory types
Disk (permanent, slow, cheap)
RAM memory (volatile, fast)
Cache (volatile, very fast)
Flash, (permanent, expensive)
Clouds *
    Most computers and cloud solutions use a combination of those types
Notes: * For Clouds the internet connection is needed

## Slide 7: CPU Cache
CPU cache:
  L1: fastest, smallest, close to the CPU
  L2: slower and larger than L1
  (L3: slower and larger than L2)
CPU first checks L1 for data, then L2(, then L3), then RAM memory, then drive
CPU
Level 1
cache
Level 2
cache
System RAM
Hard disk

## Slide 8: (S/D)RAM
SRAM and DRAM
  DRAM (Dynamic RAM is cheap (one transistor per bit) but needs refreshing
    SDRAM is a special form of DRAM that is synchronized with the clock. DDR2, DDR3 and DDR4 are examples of DRAM
  SRAM (Static RAM) needs no refreshing, but expensive (more transistors per bit)
Usually
  main memory is DRAM
  cache memory is SRAM.
Notes: Random Access Memory
Image: http://electronics.howstuffworks.com/how-to-tech/add-ram-laptop1.htm

## Slide 9: Refreshing?
Every bit is like a bucket with a hole:
  When there is water in the bucket: 1
  When bucket is empty: 0
After some time, all buckets are empty, to avoid this you have to refresh:
  Before the bucket can be empty, check if there is any water in it
  if yes, refill the bucket.
Notes: With refreshing you can think of a bucked with holes
Depletes over time -> to keep info need to refresh
This also means DRAM uses ‘more’ power

## Slide 10: SSD &(vs) HDD
SSD: no overhead of moving mechanical parts, so faster (seek time less than 0,1 msec)
Uses flash memory
Silent
Consumes less power
Lighter
Disadvantage: write-access slows over time
HDD: consists of 1 or more platters
Each platter side covered with magnetic medium
Magnetised/read by ‘read/write’ heads
Permanent or removable.
The total number of tracks on a disk is: (number of tracks on one side) * (number of sides)
The total number of sectors is: (total number of tracks) * (number of sectors per track)
The total number of bytes is: (total number of sectors) * (number of bytes per sector).
In order to read a certain sector, the disk drive must:
  position the read/write head on the right track (seek time, usually takes some msec)
  wait for the sector to pass under the read/write head (latency, takes on average ½ rotation)
  read the sector (takes the time for 1 sector to pass under the read/write head, negligible)
Total time = seek time + ½ rotation.
Assume 6000 rpm, seek time 6 msec, 1000 sectors per track
1 rotation takes 60/6000 sec = 10 msec
Waiting for the sector takes on average 1/2 rotation: 60/6000/2 msec = 5 msec
6+5 = 11 msec before reading starts
Reading 1 sector: 10/1000 = 0.01 msec (negligible).

## Slide 11: SSD vs HDD performance comparison example in cloud storage
Notes: Image: http://technofaq.org/posts/2014/11/ssd-hosting-or-hdd-hosting-which-one-to-choose/

## Slide 12: Negative numbers

## Slide 13: Binary numbers
Normal binary numbers are always positive!
But what about this C# code?
    01 int number;
    02
    03 number = 125;
    04 number = -361;

## Slide 14: Negative numbers in binary
int number = -231;
Possible by 2’s complement
Now we have 2 types of binary numbers:
  unsigned or normal binary
    only positive numbers possible
  signed or 2’s complement
    positive and negative numbers possible

## Slide 15: What does signed mean?

## Slide 16: What does signed mean?
Changes to:
Notes: Most left bit

## Slide 17: Rules for signed binary
Amount of bits must be known
Left bit (MSB) gets negative weight
Rest of bits have a positive weight

## Slide 18: Signed binary
Digits: 0 & 1
Base: 2
Weight of a most left digit: -( 2 P(osition) )
Weight of rest of the digits: 2 P(osition)
Range of values: (-2 (n-1)) ~ (2 (n-1) - 1)
Notes: Byte: -128 ~ 127
P: position
N: number of digits

## Slide 19: Signed binary to decimal
Summation of digits x weight factor
Signed 4 bits number: 11012
Result: -310
1 |  | 1 |  | 0 |  | 1
1 x -(23) | + | 1 x 22 | + | 0 x 21 | + | 1 x 20
1 x -8 | + | 1 x 4 | + | 0 x 2 | + | 1 x 1
-8 | + | 4 | + | 0 | + | 1

## Slide 20: Decimal to signed binary
Depends on the decimal value!
If positive:
Same as unsigned/nomal binary, but make sure it has the required bits
If negative:
Take the positive value
Convert to binary
Invert all the bits
Add 1

## Slide 21: Positive decimal to signed binary
To signed byte
Decimal number: 2910
Result: 000111012
1. Convert to binary: | 29 / 2 = 14, remainder 1 14 / 2 = 7, remainder 0 7 / 2 = 3, remainder 1 3 / 2 = 1, remainder 1 1 / 2 = 0, remainder 1
2. Prepend 0 till the required bits | 000 11101
Left
Right

## Slide 22: Negative decimal to signed binary
To signed byte
Decimal number: -2910
Result: 111000112
1. Make it positive: | 29
2. Convert to binary: | 0 0 0 1 1 1 0 1
3. Invert bits: | 1 1 1 0 0 0 1 0
4. Add 1 | 1 1 1 0 0 0 1 0 0 0 0 0 0 0 0 1 + 1 1 1 0 0 0 1 1

## Slide 23: Recap
Convert signed binary to decimal
Most left bit(MSB) has negative weight factor
Convert decimal to signed binary
If positive:
Same as unsigned / nomal binary, but make sure it has the required bits
If negative:
Take the positive value
Write it binary
Invert all the bits
Add 1

## Slide 24: Exercise
Convert signed byte to decimal
1111 11112
0010 01012
1000 11102
Convert decimal to signed byte
-4010
510
-5310

## Slide 25: Awnsers
Convert signed byte to decimal
1111 11112 = -110
0010 01012 = 3710
1000 11102 = -114 0
Convert decimal to signed byte
-4010 = 1101 10002
510 = 0000 01012
-5310 = 1100 10112

## Slide 26: Addition with signed binary
Same as unsigned/normal binary numbers
Unsigned
1011 + 111:
Signed (4bits)
1011 + 0111:
1 | 1 | 1 | 1 |  | 
 | 1 | 0 | 1 | 1 | 
 | 0 | 1 | 1 | 1 | +
 | 0 | 0 | 1 | 0 | 
 Carry bits
1 | 1 | 1 | 1 |  | 
 | 1 | 0 | 1 | 1 | 
 |  | 1 | 1 | 1 | +
1 | 0 | 0 | 1 | 0 | 
 Carry bits

## Slide 27: Huh, ignore stuff?
Reason:
Signed binary has a specific bit count
Consequence:
Calculated result can be wrong
1 | 1 | 1 | 1 |  |  | 
 | 1 | 0 | 1 | 1 |  | (-5)
 | 0 | 1 | 1 | 1 | + | (7)
 | 0 | 0 | 1 | 0 |  | (2)
 Carry bits
1 |  |  |  |  |  | 
 | 1 | 0 | 0 | 0 |  | (-8)
 | 1 | 0 | 0 | 0 | + | (-8)
 | 0 | 0 | 0 | 0 |  | (0)
 Carry bits
 | 1 | 1 |  |  |  | 
 | 0 | 1 | 1 | 1 |  | (7)
 | 0 | 0 | 1 | 0 | + | (2)
 | 1 | 0 | 0 | 1 |  | (-7)
 Carry bits
Notes: Side note: If the calculated result doens’t fit it’s called overflow

## Slide 28: Questions?