## Slide 1: IEO – week 9

## Slide 2: This week
IP Routing
Maintenance and drawing of the infrastructure
Notes: Applies to al electronic devices?

## Slide 3: Layered Communication: TCP/IP Protocols Overview
Physical Layer
DataLink Layer
Network Layer
Transport Layer
Application Layer
HTTP
DHCP
FTP
DNS
DHCP
Telnet
SMTP
TCP
UDP
IP
Ethernet
Wifi
Bluetooth
Bluetooth
Wifi
Ethernet

## Slide 4: IP Routing
IP Routing determines the path the data follows (through multiple networks) from the source to the destination IP address.

## Slide 5: Socrative.com Quiz
                Join the room SHAGHELANI

## Slide 6: IP Routing
Static Routing
uses preconfigured routing tables
Dynamic Routing
uses routing protocols

## Slide 7: IP Routing
Direct Route
Default Route
Host Route
Network Route

## Slide 8: IP Routing
Direct Route
We talk about a direct route when a machine can send a packet to another machine without going through a third machine.

## Slide 9: Direct Routing
ifconfig eth0 192.168.1.1
ifconfig eth0 192.168.1.2
ifconfig eth0 192.168.1.254
Network LAN_A:
192.168.1.0/24

## Slide 10: Direct Routing
Network LAN_A:
192.168.1.0/24

## Slide 11: Direct Routing
Routing Table
Direct Route

## Slide 12: IP Routing
Direct Route
Default Route
Host Route
Network Route

## Slide 13: IP Routing
Default Route
A default route is route taking effect when no other route can be determined for a given Internet Protocol (IP) destination address.

## Slide 14: Default routing
192.168.1.0/24
172.16.1.0/24
PC1 and PC2 want to communicate
with network LAN_B
PC3 and PC4 want to communicate
with network LAN_A
route add default gw 192.168.1.254
route add default gw 172.16.1.254

## Slide 15
192.168.1.0/24
172.16.1.0/24
Network 192.168.1.0/24 is connected with network 172.16.1.0/24 through default router Router1.
Network 172.16.1.0/24 is connected with network 192.168.1.0/24 through default router Router1.
Default Routing

## Slide 16: Default route
Routing Table
Direct Route
Indirect Route (G flag)
Default Route (Destination :0.0.0.0)

## Slide 17: IP Routing
Direct Route
Default Route
Host Route
Network Route

## Slide 18: IP Routing
Host Route
Host route is a route to a destination with a complete IP address.

## Slide 19: Host Route
Network 192.168.1.0/24
Network 172.16.1.0/24
PC1 wants to communicate with PC4
PC1 has a Default Route to Router 2
route add 172.16.1.2 gw 192.168.1.254
Notes: PC1 already uses default route by specifying Router2 as a default router to all external networks. If PC1 wants to communicate with PC4, it can’t use the default route, so it has to specify a different route, e.g. Host Route to PC4.

## Slide 20: Host Route
Notes: Note : The picture shows the new route with green color. To make a connection from PC1 to network PC4 and back, there should be also routing added from the PC4 to PC1. For the case of simplicity, the commands to add this routing were omitted.

## Slide 21: Host Route
Routing Table
Host Route
(flag H)

## Slide 22: IP Routing
Direct Route
Default Route
Host Route
Network Route

## Slide 23: IP Routing
Network Route
Network route is a route to a destination with a network address.

## Slide 24: Network Route
Network 192.168.1.0/24
Network 172.16.1.0/24
PC1 wants to communicate with network LAN_B
PC1 has a Default Route to Router 2
route add –net 172.16.1.0 gw 192.168.1.254 netmask 255.255.255.0

## Slide 25: Network Route
Notes: Note : The picture shows the new route with green color. To make a connection from PC1 to network LAN_B and back, there should be also routing added from the network LAN_B to PC1. For the case of simplicity, the commands to add this routing were omitted.

## Slide 26: Network Route
Route Table
Network Route
Host Route

## Slide 27: Several useful Linux networking commands
Check the routing tables:
route command
Example:
route -n
Show all routing entries of this node

## Slide 28: Several useful Linux networking commands
Sniff the traffic on a network interface:
tcpdump command
Example:
tcpdump –i eth0
Sniff the traffic on the eth0 interface

## Slide 29: Several useful Linux networking commands
Check the routing tables:
ip route show command
Example:
ip route show
Show all routing entries of this node

## Slide 30: Questions?